MIF Guideform Specifications

April 09, 2002

Feeder protection, control, monitoring and metering shall be provided in one integrated digital package for application on  feeders of any voltage level and suitable for incorporation in an integrated substation control system.

Protection and control functions shall include:

- Time overcurrent elements: one for phase, one for ground; or one single-phase

- Instantaneous overcurrent elements: two for phase, two for ground; or 2 single-phase

- Time overcurrent curve characteristics: 4 pre-configured, one user configurable

- Thermal image protection

- Cold load pickup

- Configurable breaker failure protection

- 6 outputs, four of which are configurable

- Two setting tables

Monitoring features shall include:

- 32 event record

- Oscillography

- Per phase current metering